## Slide 1: Introduction to Assembly Chapter 2

## Slide 2: Announcement
Lab
  Read before coming
  Use simulation
HW
Attendance: missing 3 labs means Fail
Makeup: you have 2 labs makeup
Late: for the lab, you have 20 min. late otherwise you will consider absent

## Slide 3: Breadboard
A breadboard is used to make up temporary circuits for testing or to try out an idea.
No soldering is required so it is easy to change connections and replace components.
Parts will not be damaged so they will be available to re-use afterwards.

## Slide 4: Topics
AVR’s CPU
  Its architecture
  Some simple programs
Data Memory access
Program memory
RISC architecture

## Slide 5: AVR’s CPU
AVR’s CPU
  ALU
  32 General Purpose registers (R0 to R31)
  PC register
  Instruction decoder
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 6: Some simple instructions 1. Loading values into the general purpose registers
LDI (Load Immediate)
LDI Rd, k
  Its equivalent in high level languages:
  Rd = k
Example:
  LDI R16,53
    R16 = 53
  LDI R19,$27
  LDI R23,0x27
    R23 = 0x27
  LDI R23,0b11101100
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 7: Some simple instructions 2. Arithmetic calculation
There are some instructions for doing Arithmetic and logic operations; such as:
  ADD, SUB, MUL, AND, etc.
ADD Rd,Rs
  Rd = Rd + Rs
  Example:
  ADD R25, R9
    R25 = R25 + R9
  ADD R17,R30
    R17 = R17 + R30
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z
Note: Rd=Destination Register and Rs= Source Register

## Slide 8: A simple program
Write a program that calculates 19 + 95
LDI R16, 19 ;R16 = 19
LDI R20, 95 ;R20 = 95
ADD R16, R20 ;R16 = R16 + R20
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 9: A simple program
Write a program that calculates 19 + 95 + 5
LDI R16, 19 ;R16 = 19
LDI R20, 95 ;R20 = 95
LDI R21, 5 ;R21 = 5
ADD R16, R20 ;R16 = R16 + R20
ADD R16, R21 ;R16 = R16 + R21
LDI R16, 19 ;R16 = 19
LDI R20, 95 ;R20 = 95
ADD R16, R20 ;R16 = R16 + R20
LDI R20, 5 ;R20 = 5
ADD R16, R20 ;R16 = R16 + R20

## Slide 10: Some simple instructions 2. Arithmetic calculation
SUB Rd,Rs
  Rd = Rd - Rs
Example:
  SUB R25, R9
    R25 = R25 - R9
  SUB R17,R30
    R17 = R17 - R30
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 11: Some simple instructions 2. Arithmetic calculation
INC Rd
  Rd = Rd + 1
Example:
  INC R25
    R25 = R25 + 1
DEC Rd
  Rd = Rd - 1
Example:
  DEC R23
    R23 = R23 - 1
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z
A =20;
A++;
B=12;
B--

## Slide 12: Data Address Space
LDS Rd, addr ;Rd = [addr]
Example:
LDS R1, 0x60
LDS (Load direct from data space)
STS addr,Rd ;[addr]=Rd
Example:
STS 0x60,R15 ; [0x60] = R15
STS (Store direct to data space)
Example: Write a program that stores 55 into location 0x80 of RAM.
Solution:
LDI R20, 55 ;R20 = 55
STS 0x80, R20 ;[0x80] = R20 = 55
Example: Write a program that copies the contents of location 0x80 of RAM into location 0x81.
Solution:
LDS R20, 0x80 ;R20 = [0x80]
STS 0x81, R20 ;[0x81] = R20 = [0x80]
Example: Add contents of location 0x90 to contents of location 0x95 and store the result in location 0x313.
Solution:
LDS R20, 0x90 ;R20 = [0x90]
LDS R21, 0x95 ;R21 = [0x95]
ADD R20, R21 ;R20 = R20 + R21
STS 0x313, R20 ;[0x313] = R20
Example: What does the following instruction do?
LDS R20,2
Answer:
It copies the contents of R2 into R20; as 2 is the address of R2.
Solution:
LDI R20, 0x53 ;R20 = 0x53
STS 0x5E, R20 ;SPH = R20
Example: Store 0x53 into the SPH register. The address of SPH is 0x5E

## Slide 13: Memory MAP

## Slide 14: Data Address Space
IN Rd,IOaddress ;Rd = [addr]
Example:
IN R1, 0x3F ;R1 = SREG
IN R17,0x3E ;R17 = SPH
IN (IN from IO location)
OUT IOAddr,Rd ;[addr]=Rd
Example:
OUT 0x3F,R12 ;SREG = R12
OUT 0x3E,R15 ;SPH = R15
OUT (OUT to I/O location)
Example:
OUT SPH,R12 ;OUT 0x3E,R12
IN R15,SREG ;IN R15,0x3F
Using Names of I/O registers
Example: Write a program that adds the contents of the PINC I/O register to the contents of PIND and stores the result in location 0x90 of the SRAM
Solution:
IN R20,PINC ;R20 = PINC
IN R21,PIND ;R21 = PIND
ADD R20,R21 ;R20 = R20 + R21
STS 0x90,R20 ;[0x90] = R20
Notes: The IN instruction has the following advantages:
1. The CPU executes the IN instruction faster than LDS. The IN instruction lasts 1 machine cycle, whereas LDS lasts 2 machine cycles.
2. The IN is a 2-byte instruction, whereas LDS is a 4-byte instruction. This means that the IN instruction occupies less code memory.
3. When we use the IN instruction, we can use the names of the I/O registers instead of their addresses.
4. The IN instruction is available in all of the AVRs, whereas LDS is not implemented in some of the AVRs.

## Slide 15: Machine Language
ADD R0,R1
LDI R16, 2
LDI R17, 3
ADD R16, R17
000011 00 0000 0001
opcode
operand
1110 0000 0000 0010
1110 0000 0001 0011
0000 1111 0000 0001

## Slide 16: Status Register (SREG)
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z
SREG:
Carry
Zero
Negative
oVerflow
Sign
N+V
Half carry
Temporary
Interrupt
H
S
V
N
C
Z
T
I
Example: Show the status of the C, H, and Z flags after the addition of 0x38 and 0x2F in the following instructions:
LDI R16, 0x38 ;R16 = 0x38
LDI R17, 0x2F ;R17 = 0x2F
ADD R16, R17 ;add R17 to R16
Solution: 1
$38 0011 1000
+ $2F 0010 1111
$67 0110 0111 R16 = 0x67
C = 0 because there is no carry beyond the D7 bit.
H = 1 because there is a carry from the D3 to the D4 bit.
Z = 0 because the R16 (the result) has a value other than 0 after the addition.
Example: Show the status of the C, H, and Z flags after the addition of 0x9C and 0x64 in the following instructions:
LDI R20, 0x9C
LDI R21, 0x64
ADD R20, R21 ;add R21 to R20
Solution: 1
$9C 1001 1100
+ $64 0110 0100
$100 1 0000 0000 R20 = 00
C = 1 because there is a carry beyond the D7 bit.
H = 1 because there is a carry from the D3 to the D4 bit.
Z = 1 because the R20 (the result) has a value 0 in it after the addition.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x23 from 0xA5 in the following instructions:
LDI R20, 0xA5
LDI R21, 0x23
SUB R20, R21 ;subtract R21 from R20
Solution:
$A5 1010 0101
- $23 0010 0011
$82 1000 0010 R20 = $82
C = 0 because R21 is not bigger than R20 and there is no borrow from D8 bit.
Z = 0 because the R20 has a value other than 0 after the subtraction.
H = 0 because there is no borrow from D4 to D3.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x73 from 0x52 in the following instructions:
LDI R20, 0x52
LDI R21, 0x73
SUB R20, R21 ;subtract R21 from R20
Solution:
$52 0101 0010
- $73 0111 0011
$DF 1101 1111 R20 = $DF
C = 1 because R21 is bigger than R20 and there is a borrow from D8 bit.
Z = 0 because the R20 has a value other than zero after the subtraction.
H = 1 because there is a borrow from D4 to D3.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x9C from 0x9C in the following instructions:
LDI R20, 0x9C
LDI R21, 0x9C
SUB R20, R21 ;subtract R21 from R20
Solution:
$9C 1001 1100
- $9C 1001 1100
$00 0000 0000 R20 = $00
C = 0 because R21 is not bigger than R20 and there is no borrow from D8 bit.
Z = 1 because the R20 is zero after the subtraction.
H = 0 because there is no borrow from D4 to D3.

## Slide 17: Assembler
Assembly
Machine
Language
assembler

## Slide 18: Assembler Directives .EQU and .SET
.EQU name = value
  Example:
.EQU COUNT = 0x25
  LDI R21, COUNT ;R21 = 0x25
  LDI R22, COUNT + 3 ;R22 = 0x28
.SET name = value
  Example:
  .SET COUNT = 0x25
  LDI R21, COUNT ;R21 = 0x25
  LDI R22, COUNT + 3 ;R22 = 0x28
  .SET COUNT = 0x19
  LDI R21, COUNT ;R21 = 0x19
  .equ once defined, cannot be redefined. It's a one-time assignment.

## Slide 19: Assembler Directives .ORG
.ORG address
.ORG 0
LDI R16, 0x25
.ORG 0x7
LDI R17, 0x34
LDI R18, 0x31
Program.asm
00 E205
01 0000
02 0000
03 0000
04 0000
05 0000
06 0000
07 E314
08 E321
09 0000
0A 0000
assembler

## Slide 20: Assembler Directives .INCLUDE
.INCLUDE “filename.ext”
.equ SREG = 0x3f
.equ SPL = 0x3d
.equ SPH = 0x3e
....
M328def.inc
LDI R20, 10
OUT SPL, R20
Program.asm

## Slide 23: Flash memory and PC register
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
E205
E314
E321
0F01
0F02
E01B
0F01
9300
0300
940C
0009
0
1
2
3
4
5
6
7
8
9
A
B
LDI R16, 0x25
LDI R17, $34
LDI R18, 0x31
ADD R16, R17
ADD R16, R18
LDI R17, 11
ADD R16, R17
STS SUM, R16
HERE:JMP HERE

## Slide 24: Fetch and execute
Old Architectures
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
Fetch
Execute
Instruct 1
Instruct 2
Instruct 3
Instruct 4

## Slide 25: Pipelining
Pipelining
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
Fetch
Execute
Instruct 1
Instruct 2
Instruct 3
Instruct 4

## Slide 26: Pipelining

## Slide 27: How to speed up the CPU
Increase the clock frequency
  More frequency  More power consumption & more heat
  Limitations
Change the architecture
  Pipelining
  RISC

## Slide 28: Changing the architecture RISC vs. CISC
CISC (Complex Instruction Set Computer)
  Put as many instruction as you can into the CPU
RISC (Reduced Instruction Set Computer)
  Reduce the number of instructions, and use your facilities in a more proper way.

## Slide 29: RISC architecture
Feature 1
  RISC processors have a fixed instruction size. It makes the task of instruction decoder easier.
    In AVR the instructions are 2 or 4 bytes.
  In CISC processors instructions have different lengths
    E.g. in 8051
      CLR C ; a 1-byte instruction
      ADD A, #20H ; a 2-byte instruction
      LJMP HERE ; a 3-byte instruction

## Slide 30: RISC architecture
Feature 2: reduce the number of instructions
AVR 8-bit architecture and supports a total of 133
  Pros: Reduces the number of used transistors
  Cons:
    Can make the assembly programming more difficult
    Can lead to using more memory

## Slide 31: RISC architecture
Feature 3: limit the addressing mode
  Advantage
    hardwiring
  Disadvantage
    Can make the assembly programming more difficult

## Slide 32: RISC architecture
Feature 4: Load/Store
  LDS R20, 0x200
  LDS R21, 0x220
  ADD R20, R21
  STS 0x230, R20

## Slide 33: RISC architecture
Feature 5 (Harvard architecture): separate buses for opcodes and operands
  Advantage: opcodes and operands can go in and out of the CPU together.
  Disadvantage: leads to more cost in general purpose computers.
CPU
Address bus
Data
Memory
Data bus
Control bus
Address bus
Code
Memory
Data bus
Control bus
Fetch
Execute
LDS R20, 0x100
ADD R20, R21
LDS R20, 0x100 ; R20 = [0x100]
ADD R20,R21 ; R20 = R20 + R21

## Slide 34: RISC architecture
Feature 6: more than 95% of instructions are executed in 1 machine cycle

## Slide 35: RISC architecture
Feature 7
  RISC processors have at least 32 registers. Decreases the need for stack and memory usages.
    In AVR there are 32 general purpose registers (R0 to R31)